## Slide 1: Optical Spectroscopy
Making light talk
by Raul D. Rodriguez & Anna Lipovka
Notes: The term ‘optical spectroscopy’ refers only to the range of interacting electro- magnetic radiation lying within the so-called ‘optical range’; a range that includes the visible and a small part of the ultraviolet and infrared spectral regions, at about 200–3000 nm. We improperly label this radiation as ‘light’, while this term only strictly refers to that radiation which can be detected by the human eye. The term ‘solids’ includes metals, semiconductors and insulators. Although most of the mate- rial treated in this book concerns the spectroscopy of centers embedded in inorganic materials, the principles described here are also applicable to molecules and atoms in the gaseous and/or the liquid state.

## Slide 2: Photonics
World market in Euros
300 million
300 billion
300 trillions

## Slide 3: Structure of the course
Section 1. Basis of Optics
Section 2. Optical Spectroscopies
Section 3. Instrumentation and Data Analysis

## Slide 4: Trivia questions
What color is the sun light?
Why is the sky blue?
Why are sunsets reddish?
How does the sun look from the ISS?
What processes are involved here?

## Slide 5
Assyrian Nimrud lens 750 BC
Nikon 2015
Ernst Abbe 1873
Notes: http://www.ancient-origins.net/ancient-technology/assyrian-nimrud-lens-oldest-telescope-world-001381
http://www.google.de/imgres?imgurl=https%3A%2F%2Fwww.microscopyu.com%2Farticles%2Foptics%2Fimages%2Fobjectives%2Fobjectivesfigure1.jpg&imgrefurl=https%3A%2F%2Fwww.microscopyu.com%2Farticles%2Foptics%2Fobjectiveintro.html&h=243&w=402&tbnid=KBvFk2xa24tbWM%3A&zoom=1&docid=3nEm4DqlhO1H2M&ei=wjtYVb2FKsL5Uu7-gKAC&tbm=isch&iact=rc&uact=3&dur=2&page=1&start=0&ndsp=31&ved=0CDAQrQMwAA
http://www.nature.com/nphoton/journal/v3/n7/full/nphoton.2009.100.html

## Slide 6
Rayleigh criterion
Fundamentally unbreakable limitation
+
?
Notes: Airy diffraction patterns generated by light from two points passing through a circular aperture, such as the pupil of the eye. Points far apart (top) or meeting the Rayleigh criterion (middle) can be distinguished. Points closer than the Rayleigh criterion (bottom) are difficult to distinguish.

## Slide 7
Ernst Abbe 1873

## Slide 8
What is it?
Where is it?
What is it made of?
…I’ll tell you how
> 6 Nobel prizes in XXI
"for the development of super-resolved fluorescence microscopy".
What is it?  Function
Where is it?  Spatial location
What is it made of?  Composition

## Slide 9: Some history
Newton 1672
Notes: From a historical viewpoint, spectroscopy arose in the 17th century after a famous experiment carried out by Isaac Newton and published in 1672. In this experiment, Newton observed that sunlight contained all the colors of the rainbow, with wave- lengths that ranged over the entire visible spectrum (from about 390 nm to 780 nm).
He actually labeled this rainbow a ‘spectrum.’ At the beginning of the 19th century, the spectral range provided by the Newton spectrum was extended with the discovery of new types of electromagnetic radiation that are not visible; infrared (IR) radiation by Herschel (1800), at the long-wavelength end, and ultraviolet (UV) radiation by Ritter (1801) at the short-wavelength end. Both spectral ranges are now of great importance in different areas, such as environmental science (UV and IR) and communications (IR).

## Slide 10: Some history
Spectrometers 19th century
Notes: Who can recognize the parts of this 19th century spectrometer?
Spectrometers
The strong development of optical spectrophotometers during the first half of the 19th century allowed numerous spectra to be registered, such as those of flame colors and the rich line spectra that originate from electrical discharges in atomic gases. With the later development of diffraction gratings, the complicated spectra of molecular gases were analyzed in detail, so that several spectral sharp-line series and new fine structure details were observed. This provided a high-quality step in optical spectroscopy.

## Slide 11: Some history
Understanding.
Niels Bohr 1913
Notes: For a long time, a large number of spectra were registered but their satisfactory explanation was still lacking. In 1913, the Danish physicist Niels Bohr elaborated a simple theory that allowed an explanation of the hydrogen atomic spectrum previ- ously registered by J. J. Balmer (1885). This constituted a large impulse for the later appearance of quantum mechanics; a fundamental step in interpreting a variety of spectra of atoms and molecules that still lacked a satisfactory explanation.
The interpretation of optical spectra of solids is even more complicated than for atomic and molecular systems, as it requires a previous understanding of their atomic and electronic structure. Unlike liquids and gases, the basic units of solids (atoms or ions) are periodically arranged in long (crystals) or short (glasses) order. This aspect confers particular characteristics to the spectroscopic techniques used to analyze solids, and gives rise to solid state spectroscopy. This new branch of the spectroscopy has led to the appearance of new spectroscopic techniques, which are increasing day by day.
In any case, it is worthwhile to emphasize the dominant role of optical spectroscopy in the investigation of solids. Indeed, the optical spectroscopy of solids appears as a nice ‘window’ onto the more general field of solid state spectroscopy.
In this chapter, we introduce the fundamentals of the main spectroscopies based on the interaction of optical beams with solid materials.

## Slide 12: Optical absorption
Electronic transitions
Notes: In an experiment, both I0and I can be measured and thus A can be deter- mined experimentally. If l and c are known, the absorption coefficient can be determined by Eq. (2.1).
The absorption coefficient is wavelength dependent and a plot of α as a function of wavelength λ is the spectrum of interest. The spectrum is often characteristic of a given sample and reflects the fundamental elec- tronic properties of the sample.
For solid samples, concentration, c, has no meaning and similar expression can be derived in terms of the thickness of the sample. The solid sample needs to be thin enough to avoid saturation of absorption

## Slide 13: Measuring UV-vis
Get inspired and draw it here
Notes: UV-visible spectrum is relatively easy to measure. However, there are still some common mistakes that beginners tend to make. First, the sam- ple concentration cannot be too high. An optical density (OD) or absorbance (A), defined as −log10(T) with T being the transmittance I/I0, should usually be around 1 and not more than 3. Too high a concentration or OD leads to saturated absorption and distorted, unreal spectrum.
Second, proper blank or background needs to be taken before the sample spectrum is measured. Ideally, one should use the same cuvette and sol- vent. If there are other species in the sample that could have absorption in the region measured but is of no interest, they should be part of the “blank” or background measurement if at all possible. Third, one needs to make sure that the sample is clear and has no floaters in a solution sample that are visible to the eye. Visible floaters will cause significant scattering and distort the measured spectrum. One common cause for floaters in nanomaterial solutions is agglomeration or aggregation of particles to form large structures with dimension on the scale of a few hundreds of nm or larger, thereby being visible to eye. If the sample contains only a small amount of aggregates, they can usually be filtered away or precipitated out by centrifugation before measurement is made.

## Slide 14
Notes: Thus, the electronic energy is a function of these multiple nuclear coordinates. A plot of the electronic energy as a function of these nuclear coordinates in more than one coordinate is often called a potential energy surface or hyper- surface. Such potential energy surfaces are essential in describing chem- ical reactions that necessarily involve nuclear motion. In principle, such potential energy surfaces can be obtained from quantum mechanical elec- tronic structure calculations by solving the electronic Schrödinger equation. In practice, this can be done usually only for small and light molecules. For large and heavy molecules, major approximations need to be introduced or models need to be developed to make the calculation practical. Nonetheless, Fig. 2.2 should serve as a convenient picture to consider electronic transitions in molecules.

## Slide 15: The refractive index
Notes: In optics the refractive index or index of refraction n of a substance (optical medium) is a dimensionless number that describes how light, or any otherradiation, propagates through that medium. It is defined as n=c/v, where c is the speed of light in vacuum and v is the speed of light in the substance. For example, the refractive index of water is 1.33, meaning that light travels 1.33 times slower in water than it does in vacuum. Wavefronts from a point source in the context of Snell's law. The region below the gray line has a higher index of refraction, and so light traveling through it has a proportionally lower phase velocitythan in the region above it.

## Slide 16: The refractive index
Notes: In optics the refractive index or index of refraction n of a substance (optical medium) is a dimensionless number that describes how light, or any otherradiation, propagates through that medium. It is defined as n=c/v, where c is the speed of light in vacuum and v is the speed of light in the substance. For example, the refractive index of water is 1.33, meaning that light travels 1.33 times slower in water than it does in vacuum. Wavefronts from a point source in the context of Snell's law. The region below the gray line has a higher index of refraction, and so light traveling through it has a proportionally lower phase velocitythan in the region above it.

## Slide 17: Total internal reflection
Notes: Figure 1.3. Evanescent wave and its measurement. (a) The evanescent wave of Fresnel arises for light incident at the angle of total internal reflection. (b) The evanescent wave disappears when continuity is restored at the boundary surface.

## Slide 18: Perfect transmission
Notes: Figure 1.3. Evanescent wave and its measurement. (a) The evanescent wave of Fresnel arises for light incident at the angle of total internal reflection. (b) The evanescent wave disappears when continuity is restored at the boundary surface.

## Slide 19: Frustrated total internal reflection
↑
λ
↓
Spectrometer
Notes: (c) Frustrated total internal reflection: part of the evanescent wave is transmitted into a propagating wave in a second prism put at a distance as close as the penetration depth of the evanescent wave. (d) Frustrated total internal reflection by a local probe tip: basic principle of near-field optical microscopy (NOM)

## Slide 20
Confocality

## Slide 21
Laser spot ̴ 2000 nm2
hν0
h (ν0 - νph)
1) Illuminate sample with laser
2) Measure intensity of scattered light at each νph
Conventional Optical Resolution:
Size of the Light Spot
Nanoparticles ̴ 40 nm