## Slide 1: EXPLOSIVE ELECTRON EMISSION: PHYSICS AND TECHNOLOGY
International Congress
ENERGY FLUXES and RADIATION EFFECTS,
Tomsk, Russia, September 16-22, 2018
Academician Gennady A. Mesyats

## Slide 2: EXPLOSIVE ELECTRON EMISSION: PHYSICS AND TECHNOLOGY
EFRE 2018
P. N. Lebedev Physical Institute, RAS (Moscow)
Tomsk Polytechnic University
Institute of Electrophysics,
UB, RAN (Yekaterinburg)
Institute of High Current Electronics,
SB, RAN (Tomsk)

## Slide 3
50 years since the discovery of the phenomenon of
explosive electron emission at Tomsk Polytechnic Institute
1. June 15, 1966: G. A. Mesyats submitted his doctoral thesis on Investigations on the generation of nanosecond high-power pulses to the Scientific Council of TPU.
2. July 2, 1966: The paper entitled “Electrooptical observations of the initiation and development of the breakdown of a short vacuum gap” was submitted to the editorial office of Zhurnal Tekhnicheskoi Fiziki (published in Zh. Tekh. Fiz., 1967, vol. 37, No. 12, pp. 2206–2208).
EFRE 2018

## Slide 4
G. A. Mesyats,
Investigations on the Generation of
Nanosecond High-Power Pulses
EFRE 2018

## Slide 5: PHENOMENOLOGY OF EXPLOSIVE ELECTRON EMISSION
Typical photos of the luminescence in a vacuum gap taken at different stages of breakdown
G. A. Mesyats and D. I. Proskurovsky Pulsed Electrical Discharge in Vacuum 1989 (Berlin: Springer Verlag)
EFRE 2018

## Slide 6: BREAKDOWN DEVELOPMENT
Streak picture of
the cathode glow
Streak picture of
the anode glow
t [ns]
EFRE 2018

## Slide 7: EMISSION CENTERS
b
c
e
f
g
a
d
i
h
Microprotrusions (a); dielectric inclusions (b); oxide and other inorganic dielectric films (c); adsorbed gas layers (d); grain boundaries emerged at the surface (e); microparticles (f); oil vapor cracking products (g); edges of craters formed upon breakdowns (h); pores and cracks (i)
EFRE 2018

## Slide 8: Microirregularities on electrode surfaces
j = AE 2 exp (-B/E)
EFRE 2018

## Slide 9: FIELD EMISSION
– Elipsoid
– Cylinder with a spherical tip
– Cone with a spherical tip (cone angle θ ~ 5–10°)
FOWLER-NORDHEIM FORMULAS
Factor of electric field enhancement
EFRE 2018

## Slide 10: FIELD EMISSION – EXPLOSIVE ELECTRON EMISSION TRANSITION
Field Emission
9.23 kV
9.83 kV
10 ns
texpl
0
0
Explosive Electron Emission Pulse
1 A
+600 V
I(t)
EFRE 2018

## Slide 11: FIELD EMISSION – EXPLOSIVE ELECTRON EMISSION TRANSITION
C
A
d
EFRE 2018

## Slide 12: FIELD EMITTER EXPLOSION
Breakdown delay time measured from the application of a voltage pulse to the explosion of the emitter
EFRE 2018

## Slide 13: ELECTRICAL EXPLOSION
To transfer a material from one energy state to another, a certain current action is required:
For the conditions of adiabatic heating κ = κ(w), ρ = ρ(w)
For c = const, κ = κ0T
where κ – resistivity, ρ – mass density, w – input energy density.
where h – specific action of current.
EFRE 2018

## Slide 14
Current density j and micropoint explosion delay time t versus electric field E
EFRE 2018

## Slide 15: ECTON PARAMETERS
Emission & evaporation zone
Liquid phase
Solid phase
Emission & evaporation zone
Liquid phase
Solid phase
b
p
p
EFRE 2018

## Slide 16
20 ns
50 ns
100 ns
300 ns
1300 ns
5000 ns
5 μm
5 μm
5 μm
2 μm
2 μm
5 μm
EFRE 2018

## Slide 17: Dimensions of droplets
tp = 35ns
tp = 10ns
tp = 50ns
tp = 100ns
tp = 300ns
Droplet diameter
d [μm]
EFRE 2018

## Slide 18: Removed mass
Mo
Mo
Mo
Mo
W
W
5ns
80ns
40ns
Cone angle
g
EFRE 2018

## Slide 19: Breakdown development
Gap closure time
X-ray pulse duration
v = d/t  2.5106cm/s
Gap spacing
ns
mm
EFRE 2018

## Slide 20: REGENERATION OF EXPLOSIVE EMISSION CENTERS
t, [ns]
t, [ps]
Cathode “polishing”
Regeneration of emission centers on a cathode
EFRE 2018

## Slide 21: STRUCTURE OF VACUUM ARC CATHODE SPOT
1 μm
EFRE 2018

## Slide 22: STRUCTURE OF VACUUM ARC CATHODE SPOT
Arc trace of cathode spot of first type (a) and second type (b). gold cathode, current 5 A (a); tungsten cathode, current 23 A, operation time 1.3 µs (b).
M.B. Bochkarev, A.M. Murzakaev, Proc. XVIIIth ISDEIV 244 (1988)
EFRE 2018

## Slide 23: MOTION OF A CATHODE SPOT
Current = 45 А
N = number of spots
B
B
Retrograde (“anti-Ampere”) direction of motion
3 μm
25 μm
EFRE 2018

## Slide 24
Micrograph of the trace of a cathode spot and
a streak picture of the spot light (left to right)
for a 4-A arc
10 ns
10 μm
20 μm
EFRE 2018

## Slide 25: Fragment of a cathode spot on a tungsten cathode
EFRE 2018

## Slide 26: Voltage Fluctuations in a short arc
100 ns
15 V
EFRE 2018

## Slide 27: Ectons in the physics of electrical discharges
Vacuum breakdown
Vacuum spark
Vacuum arc
Processes in electric contacts
Deviations from Paschen’s curve
Glow-to-arc transition
Unipolar arcs
Dielectric flashover
Runaway electrons in gas discharges
EFRE 2018

## Slide 28: PROMPT IGNITION OF A UNIPOLAR ARC
Laser spot
S Kajita et al. Nucl. Fusion 2009 49 032002, Phys. Lett. A 2009 373 4273.
EFRE 2018

## Slide 29
Electron beam generators designed to produce high-power
x-ray, microwave, and pulsed lasers
EFRE 2018

## Slide 30: SINUS: REPETITIVELY PULSED HIGH-CURRENT ELECTRON ACCELERATORS (1970s–1980s)
The accelerators were used
to produce high-power cm/mm
microwave pulses
SINUS-4, SINUS-5
Electron energy 370–420 keV
Beam current 2.5 kA
Pulse duration 25 ns
Pulse repetition rate up to 100 Hz
EFRE 2018

## Slide 31: SINUS-7: REPETITIVELY PULSED HIGH-CURRENT ELECTRON ACCELERATOR
Microwave radiating horn
Pulse-forming line
Spark gap gas flow system
Transmission line
Solenoid and Microwave oscillator
Vacuum diode
Vacuum pumping system
Energy storage capacity
up to 2 kJ
Electron energy up to 2 MeV
Beam current up to 20 kA
Pulse duration 50 ns
Pulse repetition rate up to 100 Hz
The accelerator is being actively
used in experiments on
the generation of gigawatt
microwave pulses
Cm/dm microwave pulse
power up to 5–6 GW
EFRE 2018

## Slide 32: Magnetically insulated diodes of microwave oscillators
Experimental pulse radar prototype
based on a 10-GHz relativistic
microwave oscillator with a stable
explosive-emission electron injector
EFRE 2018

## Slide 33: GAMMA: ELECTRON ACCELERATOR (1980s)
9
8
12
2
Output section of the accelerator
The electron accelerator is
based on a Marx generator.
Electron energy up to 2.2 MeV.
Beam current 30–100 kA.
Pulse duration 1–15 µs.
The electron accelerator was
used in experiments on the
generation of multigigawatt
microwave pulses
Schematic diagram of the GAMMA accelerator:
1 – Marx generator, 2 – transmission line,
3 – chopping spark gap, 4 – vacuum insulator,
5 – cathode holder, 6 – vacuum chamber,
7 – drift tube, 8 – solenoid, 9 – collector,
10 – voltage probe, 11 – current probe, 12 – case
EFRE 2018

## Slide 34: Microwave oscillator based on the SINUS 1200/50 high-current electron accelerator (delivered to China)
Beam current up to 20 kA, electron energy up to 1.7 MeV, pulse duration 55 ns
Peak radiation power up to 5 GW (1.6 GW at 100 Hz pulse repetition rate)
EFRE 2018

## Slide 35: SINUS-90: Repetitively pulsed high-voltage generator (delivered to France)
Repetitive pulsed power supply
Pulse-forming line
Gas-flow spark gap
Load
Electron energy 450 keV, beam current 7.5 kA
Pulse duration 100 ns, pulse repetition rate 200 Hz
EFRE 2018

## Slide 36: Participation of the Institute of High Current Electronics, SB, RAN in the SYRINX international project (France, Russia, USA, Israel, 1995)
The 10-stage Marx generator:
charge voltage 90 kV,
energy storage capacity 160 kJ,
current rise time 700 ns,
response time jitter 3 ns.
Load: plasma opening switch
Line pulse transformer modules:
voltage 90 kV, current 1 МА,
energy storage capacity 32 kJ,
current rise time 1 µs
EFRE 2018

## Slide 37: High-power XeCl (308 nm) laser system producing 0.5 kJ of energy per pulse (2004)
PHOTON-5 (final amplifier)
Energy per pulse: 500 J in free oscillation
mode and 250 J in amplification mode.
The gas mixture is pumped by
an electron beam (500 keV, 300 kA)
PHOTON-1
Energy
per pulse 3 J
PHOTON-3
Energy per pulse 10 J
Pulse duration 300 ns
Active gas volume
9×7×100 cm3 (Ne–Xe–HCl, 3–4 bar)
X-ray preionization
PHOTON-4
Energy
per pulse 100 J
Pulse duration
200 ns
Active gas
volume 60 liters
(Ar–Xe–HCl,
2 bar)
EFRE 2018

## Slide 38: Femtosecond XeF(C–A) laser amplifier (delivered to LPI, RAS)
Schematic of the cross-sectional
area of the amplifier output unit
Vacuum
Xe
XeF2 + N2
Xe chamber
Lead from
Marx generator
Vacuum chamber
Cathode
Foil
Laser Cell
Window
(CaF2)
EFRE 2018

## Slide 39: Multiterawatt laser pulse amplifier with a gaseous active medium (XeF(C–A), 475 nm)
(final amplifier of the THL-100 hybrid laser system)
Line pulse transformers
High-current pulse source:
two line transformers.
An electron beam (500 keV, 300 kA)
injected into xenon generates VUV
radiation (170 nm), which is used for
photodissociation pumping of
the C-level of XeF excimer molecules
Schematic of one of
the transformers and
the center laser unit
with a vacuum diode
EFRE 2018

## Slide 40
The final amplifier of the THL-100 laser system forms
an indigo radiation pulse of power 20 TW and duration 50 fs
EFRE 2018

## Slide 41: Simplified schematic of the output unit of a laser pumped by a high-current electron beam (coaxial version)
laser radiation
vacuum
to Marx generator
to Marx generator
gaseous
active
medium
electron beam
semireflecting
mirror
explosive-
emission
cathode
totally
reflecting
mirror
foil
window
EFRE 2018

## Slide 42: RADAN: COMPACT PULSE GENERATORS
RADAN-150 –
RADAN-220 series
RADAN-303
Loads: sealed-off electron and
x-ray tubes, wide-aperture
electron diodes, and magnetically
insulated diodes
Generator characteristics:
Impedance……………20–50 Ω
Output voltage……....150–300 kV
Pulse duration……….2–5 ns
Pulse repetition rate..10–100 Hz
Pulse power………….300–800 MW
Mass……………………8–27 kg
EFRE 2018

## Slide 43: Magnetically insulated diodes of microwave oscillators
Compact relativistic 38-GHz and 70 GHz microwave oscillators
with stable cold-cathode electron injectors
EFRE 2018

## Slide 44: RADAN-303B-based sterilizer
Protection cell with the door open
RADAN-303B-based desktop setup
for laboratory elaboration of radiation
processing and surface sterilization
technologies.
Electron energy 150 keV, mass 60 kg
The dual radiation source
with the case removed
EFRE 2018

## Slide 45: CATHODOLUMINESCENCE SPECTRUM ANALYZER
Luminosity of the crystal luminescence centers is proportional to the power of the exciting e-beam.
A short high-power electron beam is used for nondestructive precision spectral analysis.
Luminosity
Luminosity
Wavelength, nm
Wavelength, nm
Impurity
crystals
Natural
corundum
Synthetic
corundum
EFRE 2018

## Slide 46: RADAN: PORTABLE HIGH-POWER MILLIMETER MICROWAVE OSCILLATORS
Quasistationary relativistic
8-mm BWT:
Microwave power 20–100 MW
Pulse duration 3 ns
Pulse repetition rate up to 10 Hz
Nonstationary relativistic
8-mm BWT:
Microwave power 300–1000 MW
Pulse duration 0.3 ns
Pulse repetition rate
up to 3.5 kHz
EFRE 2018

## Slide 47: PORTABLE PULSED X-RAY GENERATORS
X-ray Film
Cassette
The small-sized portable nanosecond and
subnanosecond 100–200-keV generators
are intended for research and practical uses
Portable x-ray flaw detector
Subnanosecond x-ray apparatus
Self-contained x-ray introscope
EFRE 2018

## Slide 48: PROCESSING SYSTEMS BASED ON NANOSECOND ELECTRON ACCELERATORS
The SINUS-6 accelerator
as a unit of the stand
for thorough elaboration of
laquer coating polymerization
technology
Electron energy: 400 keV
E-beam current: 8 kA
Pulse duration: 25 ns
Pulse repetition rate: up to 400 Hz
EFRE 2018

## Slide 49: PROCESSING SYSTEMS BASED ON NANOSECOND ELECTRON ACCELERATORS
Electron-beam sterilizers
for powder materials
based on compact accelerators
of the SINUS series
Designated areas:
drug and food production
Can be used for sterilization
of thermolabile powders
EFRE 2018

## Slide 50
Since 1970s…

## Slide 51: THANKS FOR ATTENTION !